## Slide 1: SONiC-VPP
Shashidhar Patil shaship@cisco.com
Sameer Nanajkar sananajk@cisco.com

## Slide 2: What is SONiC ?
Software for Open Networking in the Cloud
Is an open-source network operating system based on Linux
SAI (Switch Abstraction Interface) API for dealing with forwarding engine in a platform independent way
Primarily developed by Microsoft for data center switches in Azure cloud
Is now a community driven project
SONiC architecture , wiki and SAI will be of help

## Slide 3: Why SONiC-VPP ?
SONiC lacks a software forwarding engine which
  Is feature rich
  Is performant
  Is open sourced and community driven
  Runs on multiple commodity hardware
In summary VPP fits the bill

## Slide 4: Use Cases
SONiC Development vehicle
Virtual Gateway
Cloud Router
Stateful Services (NAT, IPsec, etc.)

## Slide 5: Abstraction
Operating System
Hardware
NIC
Adapter Host 1
VPP Adapter
SAI Interface
SONiC
VPP
VPP Binary API
Name | Description
Control Stack | Upper Applications (e.g. NOS)
Adaptor | Pluggable vendor code module that implements BSP APIs for a platform
Adaptor Host | Software component of a control stack that loads Adaptor

## Slide 6: Realizing SONiC-VPP

## Slide 7: Deployment Models
SONiC
VPP
Foundational NIC
Server
Single Host
Linux Kernel
SONiC
VPP
Server
Linux Kernel
DPU
SONiC
VPP
Server A
Linux Kernel
NIC
Server B
Single Host w/ DPU
Multi Host
Legend
1:1 SONiC instance – VPP instance mapping
Focus of this talk
Linux Kernel
Linux Kernel
VPP IPC
Netlink
VPP

## Slide 8: SONiC-VPP Development Model
What constitutes SONiC-VPP repo ?
Makefiles, scripts, docker templates etc. which define VPP as a platform
Saivpp library implements SAI API to VPP translation, VPP Binary API etc.
How SONiC-VPP build works ?
“make sonic” and “make sonic_vm” build the SONiC images docker-sonic-vpp.gz and sonic-vpp.img.gz rept.
The build script pulls main SONiC repo and applies the patches required to build SONiC-VPP image
Prebuilt VPP package is downloaded from the internet during the build
Built SONiC images are in $REPO_DIR/build/sonic-buildimage/target/
How to manually test SONiC-VPP images ?
Testing single container image is simple
  Load single container docker image (docker-sonic-vpp.gz)
  Create virtual interfaces (veth pair) and assign address to one end of veth pair
  Invoke “start_sonic_vpp.sh -n SOME_NAME –I vpp1,vpp2”, Voila !!!
  Please refer to a simple topology test with Single container image
QEMU VM Image testing explained here
More test scenarios mentioned in the docs directory

## Slide 9: Development testing
What Sanity tests cover SONiC-VPP ?
CI pipeline for images build in place
Basic Sanity tests for interfaces, routing and routing protocols will be integrated to the CI pipeline
SONIC-PTF driven topologies (T0, T1) testing will be enabled in future once feature parity between SONiC and VPP is reached
SONIC testbed topologies
T0 Topology
T1 Topology
DUT – Device Under Test VM - Virtual Machine

## Slide 10: How VPP starts ?
Linux Host
start_sonic_vpp.sh
docker
vpp_init.sh
vpp
VPP Config
startup.conf
VPP config
VPP in Single container (Simple Topo)
SONiC VM
syncd.service
docker
vpp_init.sh
vpp
VPP config
startup.conf
VPP config
VPP in a VM (Simple Topo)
Container
Container
sonic_vpp_cfg.sh
syncd
IPC
syncd
IPC
ONESHOT

## Slide 11: Control Plane – VPP interactions
Syncd and vpp processes are part of the same container
Syncd connects to VPP via vpp api unix socket
SONiC
VPP
VPP Main
Binary API
VPP Workers
Data path structures
syncd
ASIC_DB
VPP binary API lib
libsaivpp.so
Config State
Xlate logic

## Slide 12: Control Plane – VPP config flow
SONiC-VPP uses synchronous API handling mechanism
config objects written to DB after OK received from syncd
SWSS
libsaivpp.so
VPP
Req
Resp / Notification
Config
Redis
Config Notify
Sync
Config Resp / Notify
Error handling logic
Events
SONiC
syncd
Config OK
Yes
No
1
2
3
4
5

## Slide 13: API Semantics
VPP
Binary API is a message passing API
Method types
  Request/Reply (1 req –> 1 reply)
  Dump/Detail (1 req –> N replies)
  Events (1 req –> 1 reply + N notifications)
Large number of APIs (~1900)
SAI
Fixed operations on a set of object types
~ 100 object types
Translation of SAI APIs to VPP APIs
  Non-trivial in some scenarios
  Requires an intelligent glue logic (maintain state, etc.)

## Slide 14: Sample API Translation (IP Routes)
SONIC Operation | SAI API | VPP API logic
Route Add | create_route_entry | vl_api_ip_route_add_del_t{ADD, route}
Route Modify | set_route_entry_attribute | vl_api_ip_route_add_del_t{DEL, old_route}, vl_api_ip_route_add_del_t{ADD, new_route}
Route Delete | remove_route_entry | vl_api_ip_route_add_del_t{DEL, route}
Route Get | get_route_entry_attribute | vl_api_ip_route_lookup_t{prefix}

## Slide 15: ARP Flow
Port 0
NIC
Port 1
VF 1
VF2
Ethernet 0
Ethernet 1
Linux Kernel
VPP
Linux CP plugin
SONIC
MAC-1
Front Panel Physical Ports
Host A
172.16.1.2/24
Host B
172.16.2.2/24
172.16.2.1/24
172.16.1.1/24
MAC-2
1
2
3
3
4
ARP Reply
5
7
Step | Description
1 | ARP Broadcast
2 | Internal broadcast to VFs (in NIC)
3 | Linux CP /Punt plugin uses VF to Host IF mapping to forward
4 | Linux kernel does ARP resolution & sends reply on Ethernet 0
5 | Linux CP plugin sends ARP reply to VF1
6 | VF1 sends to associated PF (Port 0)
7 | NIC sends ARP Reply on wire to Host A
6
Punt plugin

## Slide 16: Host Path Flow
Port 0
NIC
Port 1
VF 1
VF2
Ethernet 0
Ethernet 1
Linux Kernel
VPP
MAC-1
Front Panel Physical Ports
Router A
172.16.1.2/24
172.16.2.1/24
172.16.1.1/24
MAC-2
1
2
3
6
7
1 | BGP Control packet from Router A
2 | NIC redirects to VF1
3 | Linux CP /Punt plugin uses VF to Host IF mapping to forward to Ethernet 0
4 | Linux kernel send via Socket IF to BGP process
5 | BGP process reply via socket IF
6 | Ethernet 0 sends packet via Linux CP plugin to VF1
7 | NIC send BGP response to Router A
SONiC
BGP
4
5
Linux CP plugin
Punt plugin

## Slide 17: Traffic Flow
Port 0
NIC
Port 1
VF 1
VF2
Ethernet 0
Ethernet 1
Linux Kernel
VPP
SONIC
MAC-1
Host A
172.16.1.2/24
Host B
172.16.2.2/24
MAC-2
Fm
F1
Legend
Data path Feature
+ Caveats apply

## Slide 18: IP Route Add Flow
zebra
shell
Netlink
Route add
SONiC
NetLink Route add
fpmsync
APPL_DB
SWSS
Linux Kernel
Netlink plugin
P4RT
Netlink Route Add
intfmgrd
Interface IP address cfg
ASIC_DB
syncd
libsaivpp.so
VPP Main
VPP
ROUTE_TABLE, P4RT_TABLE
A
B
A
vpp linux_nl plugin
B
VPP Binary API
vl_api_ip_route_add_del_route_t
VPP bin API lib
Legend
New code / Modifications

## Slide 19: Current Status
Source code at sonic-net
Build generates (via “make sonic” and “make sonic_vm”
  Single container image (docker-sonic-vpp.gz)
  QEMU VM image (sonic-vpp.img.gz)
Support for virtual(veth) and physical network interfaces (including SR-IOV VFs)
Basic features supported
  Interfaces and sub-interfaces configuration and statistics
  VRF and routes configuration
  IPv4/IPv6 Routing, IPv4 multipath routing (ECMP)
  Routing Protocols (BGP)
SONiC CI enabled (link)

## Slide 20: Roadmap
Phase I
Interfaces and sub interfaces
IPv4, IPv6 routing, adjacencies
VRF and routing protocol support(BGP)
Build system for single container and VM images
Basic test framework
Roadmap details
Phase II
VPP configurability
Debugging support
SONiC-VPP migration to debian bullseye distribution
VPP migration to bullseye 23-xx-release
Loopback interface provisioning
VLAN, port channel (LAG)
ACL support
Phase III
L2 Switching, STP
QOS, Policer
OSPF, IS-IS
Phase IV
IPsec
NAT
MACSEC
Stateful Firewall